## Slide 1: ON POLICY MULTI-AGENT REINFORCEMENT LEARNING FOR 6G EDGE-CLOUD COMPUTING
Kan Ziyang
A0326643A
Supervisor: Prof. Tham Chen Khong
March 2026

## Slide 2: Abstract
Task offloading in 6G edge-cloud systems must coordinate execution placement and wireless PRB reservation
Proposed MAPPO scheduler for joint task offloading and PRB allocation in LOCAL-EDGE-CLOUD architecture
MAPPO achieves 99.96% success rate vs 90.39% for best heuristic (ROUND_ROBIN)
PPO baseline reaches 99.94%, showing on-policy RL effectiveness
Adaptive PRB control is the dominant source of performance gain
MAPPO provides narrower reliability-oriented advantage over PPO

## Slide 3: Research Questions
1. Can on-policy RL improve QoS and system efficiency over heuristic schedulers when destination and PRB are jointly optimized?
2. Is adaptive PRB allocation the dominant source of performance gain relative to other MAPPO design choices?
3. Does MAPPO provide meaningful advantage over shared-policy PPO baseline in deadline-sensitive reliability?

## Slide 4: Main Contributions
Joint task-offloading and PRB-allocation formulated as Dec-POMDP
MAPPO framework with CTDE: per-device actors + centralized critic
Shared-policy PPO baseline under same environment interface
Extended PureEdgeSim with PRB-aware networking and Java-Python co-simulation
Comprehensive evaluation against heuristic and learning baselines

## Slide 5: Background: 6G and Mobile Edge Computing
6G integrates intelligence, communication, and distributed computing
MEC reduces latency by moving computation closer to users
Radio-resource allocation is central to edge-cloud orchestration
Scheduler must jointly determine WHERE and HOW MUCH wireless resource
Without reasonable PRB allocation, attractive compute destination can produce poor outcome

## Slide 6: Why Multi-Agent Reinforcement Learning?
RL improves through interaction rather than analytical model
Devices interact through shared PRBs, edge queues, and compute resources
One device's choice affects others - naturally multi-agent problem
MARL enables local decision-making while learning cooperative behavior
Partial observability + shared constraints + system trade-offs

## Slide 7: Related Work Comparison

## Slide 8: Related Work Comparison

## Slide 9: Three-Tier System Architecture
200m × 200m area with 160 devices, 4 edge data centers, 1 cloud node

## Slide 10: Extended PureEdgeSim Architecture
Four coordinated layers: simulator extensions, RL interface, runtime support, telemetry

## Slide 11: Event-Driven Task Lifecycle
Decisions triggered when tasks arrive, preserving event-driven semantics

## Slide 12: Java-Python Training Architecture
Training mode: Python launches Java, synchronous TCP JSON protocol

## Slide 13: Simulation Configuration
• Area: 200m × 200m
• Devices: 160 (30% smartphone, 30% sensor)
• Simulation time: 30 minutes
• Mobile speed: 1.4 m/s
• Edge coverage: 120m
• Cloud distance: 160m
• WLAN bandwidth: 5000 Mbps
• Total PRB blocks: 5000
• Max PRBs per task: 50
• Reference distance d₀: 20m
• Distance exponent α: 0.5
• VM policy: SPACE_SHARED

## Slide 14: PRB-Based Communication Model
Total capacity: 5000 Mbps discretized into 5000 PRB blocks
Bandwidth = (BW_WLAN / PRB_total) × blocks × min(1, (d₀/max(d,d₀))^α)
RL algorithms: fixed PRB reservation before transmission
8 discrete PRB bins: {0.02, 0.05, 0.10, 0.20, 0.40, 0.60, 0.80, 1.00}
Non-RL algorithms: dynamic PRB allocation by simulator
Cloud uses fixed equivalent distance of 160m

## Slide 15: Energy Model
Wireless energy: EEZC protocol with free-space and multipath models
E_tx = E_elec·B + E_fs·B·d² (d ≤ d₀) or E_mp·B·d⁴ (d > d₀)
CPU energy: linear utilization model
ΔE_cpu = [P_idle + (P_max - P_idle)·u] / 3600 · Δt
Online standardization via EMA for RL reward stability
Total energy = CPU energy + wireless energy

## Slide 16: Dec-POMDP Formulation
Agent set N: all task-generating devices
Observation o_i: task demand, device state, destination features, feasibility mask
Action a_i = (dest, prb): execution destination + PRB reservation level
Global state s: aggregated load, energy, PRB usage
Objective: minimize weighted cost of failures, latency, energy, PRB, fallback
Constraints: feasible destinations, PRB budget, deadline satisfaction

## Slide 17: MAPPO CTDE Framework
Centralized training with decentralized execution

## Slide 18: Observation and State Design
Agent observation (13D): task demand (5) + device state (4) + network context (4)
Destination features (11D per dest): load, capacity, delay, distance, tier indicators
Destination mask: suppresses infeasible destinations
PPO critic state (27D): agent obs + aggregated system statistics
MAPPO critic state (41D): base state + destination distribution + PRB distribution
All features normalized to [0,1] or [-2,2]

## Slide 19: Action Space and Fallback
Composite action: (destination, PRB bin)
Destination: local(0) → edge DCs (sorted by ID) → cloud
PRB bins: 8 discrete levels mapping to {1, 2, 5, 10, 20, 30, 40, 50} blocks
Local execution forces PRB=0, log-prob and entropy zeroed
Destination fallback: if infeasible at execution, use shortest estimated completion
Fallback transitions excluded from PPO updates, penalized in reward

## Slide 20: Reward Function Design
R = -5.0 if task fails
R = 5.0 - L̃ - 2.0Ẽ - 1.5B̃ - 1.5Z if task succeeds
L̃: latency ratio (realized / deadline), clipped to [0,2]
Ẽ: online-standardized energy via EMA (α=0.01)
B̃: normalized PRB cost (requested / max), clipped to [0,1]
Z: fallback indicator (1 if fallback triggered, 0 otherwise)
QoS-oriented: prioritizes success and timely completion

## Slide 21: MAPPO Network Architecture
Agent embedding: 16D learnable per device (MAPPO only)
Agent encoder: 2-layer MLP (29→128→128) with tanh
Destination encoder: 2-layer MLP (139→128→128), shared across destinations
Destination head: linear projection (128→1), masked softmax
PRB head: 2-layer MLP (256→128→8), conditioned on selected destination
Centralized critic: 3-layer MLP (41→256→256→1) for MAPPO, (27→256→256→1) for PPO

## Slide 22: Training Algorithm
PPO with clipped surrogate objective, ε=0.1
Immediate-return design: G_t = r_t, Â_t = r_t - V(s_t)
Entropy annealing: 0.02 → 0.002 over 40 episodes
Learning rate: 3×10⁻⁴ for both actor and critic
4 PPO epochs per update, minibatch size 1024
Fallback transitions excluded from updates
Training: 40 episodes, ~2.53 hours total

## Slide 23: MAPPO Training Progress
Success rate: 57.85% (ep1) → 99.91% (ep40), stable plateau after ep13

## Slide 24: MAPPO Three-Seed Evaluation
Seed 9001: 99.8901% success
Seed 9002: 99.9390% success
Seed 9003: 99.9421% success
Mean: 99.9237% ± 0.0238%
Avg total time: 4.5284s
Energy: 227.64 Wh
Strong cross-seed robustness
All three runs tightly clustered
No large deviations
Consistent generalization
Stable policy behavior

## Slide 25: MAPPO Evaluation Overview (Seed 9001)
51.73% cloud, 19.81% local, 28.46% edge; PRB: 72.76% use 1-block

## Slide 26: MAPPO Runtime Resource Dynamics
Moderate stable PRB reservation, balanced CPU utilization across tiers

## Slide 27: Device Count Scalability Study
80/160/240 devices converge; 320 devices fail due to infrastructure saturation

## Slide 28: Device Count Evaluation Results
80 devices: 99.75% success
160 devices: 99.77% success
240 devices: 99.55% success
320 devices: 54.06% success
Graceful scaling 80→240
Sharp collapse at 320
Delay failures:
• 80: 86
• 160: 154
• 240: 451
• 320: 61,899 (137× jump)
Infrastructure saturation,
not optimization failure

## Slide 29: Ablation Study: NoEmbedding vs FixedPRB
NoEmbedding:
• Success: 99.8148%
• Delay failures: 123
• Energy: 227.73 Wh
• Small controlled degradation
• Removes 16D agent embedding
• Slightly more aggressive PRB
FixedPRB (10 blocks):
• Success: 92.3822%
• Delay failures: 5127.67
• Energy: 309.26 Wh
• Structural failure
• Disables adaptive PRB
• Systematic mismatch

## Slide 30: Ablation Study Conclusions
Adaptive PRB control is the DOMINANT contributor to performance
Removing PRB adaptation: 99.92% → 92.38% success, 7.5pp drop
Removing agent embedding: 99.92% → 99.81% success, 0.11pp drop
Agent embeddings provide smaller but consistent reliability refinement
MAPPO value = joint offloading-PRB learning + agent conditioning
FixedPRB shows systematic inability to manage compute-radio contention

## Slide 31: Offline Baseline Comparison (Fixed Seed)
MAPPO: 99.96% | PPO: 99.94% | ROUND_ROBIN: 90.39% | CLOUD: 64.64% | LOCAL: 45.36%

## Slide 32: Baseline Comparison Highlights
MAPPO: 99.96% success, 4.56s time, 231.26 Wh, 20 delay failures
PPO: 99.94% success, 4.49s time, 231.38 Wh, 36 delay failures
ROUND_ROBIN: 90.39% success, 5.83s time, 298.26 Wh, 6452 failures
RL policies: 9.58pp success gain, 1.28s faster, 67 Wh less energy
RL bandwidth: 4.07 Mbps vs RR: 77.26 Mbps (19× reduction)
Coordinated three-tier usage vs mechanical single-tier overload

## Slide 33: Runtime Success Trajectories
MAPPO/PPO: flat near 100%; ROUND_ROBIN: gradual decline to 90%

## Slide 34: Runtime Destination Distribution
MAPPO/PPO: cloud-dominant three-tier; RR: larger local fraction, flatter edge split

## Slide 35: CPU Utilization Comparison
MAPPO/PPO: balanced loading; RR: edge near saturation causing queuing delays

## Slide 36: Delay Distribution Comparison
MAPPO/PPO: narrow band well below deadline; RR: wider spread with tail violations

## Slide 37: Task Failure Accumulation Over Time
MAPPO/PPO: flat curves (20/36 failures); RR: linear accumulation (6452 failures)

## Slide 38: MAPPO vs PPO: Detailed Comparison
Three-seed means:
• MAPPO: 99.9237% ± 0.0238%
• PPO: 99.9436% ± 0.0137%
PPO marginally stronger on:
• Mean success rate
• Variance
• Mean total time
• Mean energy
MAPPO advantages:
• Fixed-seed: 20 vs 36 failures
• Better deadline reliability
• Structurally aligned
• Per-device formulation
MAPPO = methodologically
better-matched scheduler

## Slide 39: Answer to Research Question 1
Q1: Can on-policy RL improve QoS and system efficiency over heuristics?
YES - Strong positive evidence:
• MAPPO/PPO: 99.9%+ success vs 90.39% best heuristic
• 9.58pp success gain, 1.28s faster, 67 Wh less energy
• 19× reduction in bandwidth occupation (4.07 vs 77.26 Mbps)
• Joint destination-PRB control improves both QoS and efficiency

## Slide 40: Answer to Research Question 2
Q2: Is adaptive PRB allocation the dominant source of gain?
YES - Ablation evidence is clear:
• FixedPRB: 99.92% → 92.38% success (7.5pp drop)
• NoEmbedding: 99.92% → 99.81% success (0.11pp drop)
• Adaptive PRB control is 68× more important than agent embedding
• Joint offloading-PRB learning is the key principle

## Slide 41: Answer to Research Question 3
Q3: Does MAPPO provide meaningful advantage over PPO?
QUALIFIED YES - Narrower reliability-oriented advantage:
• PPO marginally stronger on aggregate three-seed means
• MAPPO: fewer residual deadline failures (20 vs 36 fixed-seed)
• NoEmbedding ablation: agent conditioning improves reliability
• MAPPO = structurally better-matched per-device formulation
• Not universally superior, but methodologically aligned

## Slide 42: Key Findings Summary
On-policy RL substantially outperforms heuristic schedulers
Adaptive PRB control is the dominant design factor
MAPPO provides reliability-oriented advantage over PPO
Graceful scaling 80→240 devices, collapse at 320 (infrastructure limit)
Joint communication-computation control is essential
MAPPO = methodologically aligned per-device scheduler

## Slide 43: Limitations
Simulation-based evidence, gap to real 5G/6G deployment
Claims tied to tested workload range and infrastructure
320-device saturation shows capacity boundary, not infinite scalability
Full-task offloading only, no partial offloading
Limited to LOCAL-EDGE-CLOUD, no mist layer or device-to-device
PPO artifacts lack per-decision trajectory exports for symmetric comparison

## Slide 44: Future Work
Map capacity boundary systematically across device density and infrastructure
Preserve symmetric behavioral artifacts for PPO and MAPPO
Extend to partial offloading with joint task partitioning
Expand architecture to include mist layer and neighboring-device execution
Reduce simulation-to-reality gap with realistic traces or hardware testbed
Broader robustness validation across seeds, traffic patterns, topologies

## Slide 45: Conclusion
Joint task offloading and PRB allocation formulated as Dec-POMDP
MAPPO framework with CTDE achieves 99.96% success rate
Adaptive PRB control is the dominant contributor to performance
MAPPO provides reliability-oriented advantage, structurally aligned
On-policy RL is effective within tested capacity envelope
Extended PureEdgeSim provides end-to-end training/evaluation pipeline

## Slide 46: Thank You
Questions?